## Slide 1: [PROPOSED] Presentation Outline ---------------------------------------------[---🚨---DELETE OR HIDE BEFORE PRESENTING---🚨---]---------------------------------------
# | Owner | Title | Content Focus
1 | Chris | Intro & Motivation | • Tokamaks are a leading technology for commercial fusion energy. • A major hurdle is "plasma disruptions" (sudden losses of confinement that damage hardware). • Safely terminating a discharge requires real-time control over plasma current ($I_p$) and internal inductance ($L_i$).
2 | Chris | The Physics Problem: Modeling Plasma Dynamics | • Partial differential equations are too slow for real-time, sub-millisecond control. • The Romero (2010) model derived an ODE approximation to solve this. • While energy and flux equations are exact, the voltage ($\dot{V}$) equation is a flawed first-order approximation.
3 | Phil | AI Methodology: Hybrid Neural ODEs (Teach Each Other) | • Neural ODEs output time derivatives instead of states, naturally coupling with physics. • We are building on "RomeroNNV," a hybrid model using a neural net to learn the unknown $\dot{V}$ dynamics. • Core Goal: Use Symbolic Regression (SR) and SINDy to turn this black-box network into an interpretable equation.
4 | Phil | Project Goals & Workflow | • Goal 1: Reproduce Wang's model across Julia, Python/JAX, and Python/PyTorch. • Goal 2: Use the trained models to generate a dense, regularly-sampled synthetic dataset (bypassing experimental data gaps). • Goal 3: Apply SR and SINDy to discover a new, physical equation for plasma voltage dynamics.
5 | Phil | Preliminary Results: JAX Implementation & SINDy | • Successfully established a stable training loop and reproduced RomeroNNV. • Achieved target Mean Absolute Percent Error (4.27% for $L_i$, 2.83% for $I_p$). • Began preliminary exploration of applying SINDy to data residuals.
6 | Chris | Preliminary Results: Julia Implementation & The Diagnostics | • Breakthrough: The pure neural MlpODE_v70 achieved the best $L_i$ and $I_p$ tracking metrics across all three implementations. • Diagnostic Check: Built a novel $dV/dt$ correlation diagnostic to verify if the physics were actually learned. • The Result: $R^2$ remained near zero; the networks used $V$ as a free latent variable rather than learning the physical dynamics.
7 | Tino | Preliminary Results: PyTorch Implementation & The Second Obstacle | • Evaluated the architectures using a strict full-trajectory continuous integration. • Compounding error over a full shot provided a strictly harder evaluation task. • Under this continuous evaluation, the pure neural network (MlpODE) tracked $I_p$ better than the hybrid model.
8 | Tino | The Roadblock: The Data Bottleneck | • Root Cause: The underlying finite-differenced voltage signal is completely noise-dominated (even pure physics shows $R^2 \approx 0.0002$). • SINDy Dilemma: Applying SINDy to these data residuals will inherit the exact same noise problem. • Pivot: We are framing this as a definitive, clean negative result rather than forcing equation discovery on unviable data.
9 | Tino | Next Steps & Feedback | • Finalize cross-framework comparisons to cement MlpODE_v70 as the strongest reproduction. • Anchor the final paper on this positive engineering result paired with our negative diagnostic result. • Feedback: How have peers handled downstream tasks (like equation discovery) becoming mathematically unviable due to dataset noise late in a project?
10 | Tino | Thank You & Resources | Citations / References Slide; github, etc

## Slide 2: Reproducing & Diagnosing a Hybrid Neural ODE for Plasma Current Dynamics in the Alcator C-Mod Tokamak ENGR 521 A: Machine Learning For Engineering Project - Spring 2026
Phillip Prior
[pjr32@]
Chris Billingham
[cmb27@]
Tino Wells
[tinow@]

## Slide 3
Notes: ●Fusion power has been the longest-running "almost there" story in energy. But the last few years changed the timeline — in 2022, the National Ignition Facility at Lawrence Livermore achieved net energy gain, and private companies are now building fusion devices at a pace nobody expected.
●The top diagram shows the most common fusion reaction: deuterium and tritium fuse into helium and a neutron, releasing energy. Below is the inside of Alcator C-Mod, the MIT tokamak that produced the experimental data we use. A tokamak holds a plasma hotter than the sun inside a magnetic bottle — and that plasma is violently unstable. Lose control for a few milliseconds, and it dumps enormous energy onto the reactor walls. Preventing that requires real-time decisions, faster than traditional physics control systems can run.
●That's the gap AI can potentially fill. But a machine learning model that just fits data, without respecting the physics, can't be trusted in conditions it hasn't seen.

## Slide 4
Notes: ●This is exactly the problem addressed by Allen Wang and colleagues in their 2023 NeurIPS paper. Using experimental data from Alcator C-Mod, they model three coupled plasma quantities — internal inductance, plasma current, and loop voltage. Two of these follow exact physics equations derived by Romero in 2010. But the third — the loop voltage — only has an approximate expression, shown here as roughly proportional to the voltage itself plus a driving term. Wang's key IDEA: replace that weak approximation with a neural network, while keeping the trustworthy physics for the other two.
●Our base goal was to independently reproduce Wang's models in three separate frameworks — PyTorch, JAX, and Julia — to confirm the result holds across implementations. Then we asked a more ambitious question: could we go beyond Wang, and use equation-discovery tools — symbolic regression, or SINDy — to recover an actual mathematical expression for that missing voltage equation? That would turn a black box back into interpretable physics.

## Slide 5: AI Methodology: Hybrid Neural ODEs
Phil
Neural ODEs
SINDy / Symbolic Regression
Data:
Candidate Equations
Sparse regression/STLS
Interpretable Dynamics
Learn unknown dynamics from time series data
Question: Did the Neural ODE learn hidden plasma structure that can be simplified into interpretable equations?

## Slide 6: Project Goals & Team Workflow
Phil
Goal 1
  Reproduce Romero, RomeroNN, and MlpODE
    Julia – Chris
    Python/Jax – Phil
    Python/PyTorch – Tino
Goal 2
  Trained RomeroNN model to generate synthetic data
Goal 3
  Apply Symbolic Regression (Chris) and SINDy (Phil) to discover a new physical equation for plasma voltage dynamics

## Slide 7: Preliminary Results: JAX & SINDy
Phil
Source | Model Type | Endpoint – Li | EndPoint - Ip
JAX | RomeroNN | 4.27% ±3.71% | 2.83%±1.52%
 | RomeroModel | 6.03%±5.36% | 9.52%±13.75%
 | MlpODE | 3.05%±2.58% | 2.28%±1.94%
Example: Single Plasma shot
RomeroNN & MlpODE cloned models replicate plasma dynamics from Wang et al (2023)
Reasonable reproduction of plasma dynamics but some differences
Question: Is VromeoNN capturing hidden low order structure missing from RomeroMODEL?

## Slide 8: Preliminary Results: JAX & SINDy
Phil
Measured V differs from Analytic near end of shot
VromeroNN is capturing plasma shot dynamics
The Neural ODE captured dynamics that could not be reduced to a simple sparse polynomial equation.

## Slide 9
Notes: So — did it work? Mostly yes, with one important twist. I reproduced Wang's model in Julia, and it tracks the two physics-governed quantities — inductance and current — as accurately as the original paper, across both error metrics in Table 1. In fact, one of my configurations beats Wang's published numbers outright.

## Slide 10: Preliminary Results: Julia
[Insert Text Here]
Chris
Notes: But then I tested the part that matters for equation discovery. If we want symbolic regression to find the voltage equation, the network first has to actually learn the voltage according to its physics. So, we ran a diagnostic Wang didn't: we compared the network's predicted voltage dynamics against the real data.
The answer is in Table 2 and the scatter plots in Figure 3. The correlation is essentially zero — no better than noise. The network reproduces inductance and current beautifully while treating voltage as a free variable it can set to whatever makes those two fit best.

## Slide 11
Notes: This tells us two things. First, symbolic regression is not a viable path here — you can't extract a meaningful equation from a network that didn't learn the underlying signal. And second — we tested whether forcing the issue would help, by adding voltage directly into the training objective. It didn't. The correlation stayed essentially zero.
So, the model is fast and accurate where it counts — but it's fitting the voltage, not understanding it. Finding that limit, clearly and quantitatively, is itself a necessary part of applying AI to scientific research.

## Slide 12: Preliminary Results: PyTorch
Near-perfect Ip trajectory overlap: MlpODE model achieved a 0.21% MAPE
MlpODE tracks Ip better than RomeroNNV
Rigorous Continuous Evaluation: Optimized, evaluated models using full-trajectory (trapezoidal-rule) integration over the entirety of each 28-step continuous shot
Tino

## Slide 13: Preliminary Results: PyTorch
For full-shot / trajectory :
Rapid Early Descent for the NN: quickly find a way to manipulate V, minimizing loss for Ip & Li; curve drops fast and smooth
Stagnation for Physics Models: A physics/hybrid model cannot arbitrarily bend V into a non-physical shape just to lower the loss. Because the underlying data is noisy, the physics equations will struggle to fit it, leading to early stagnation or a high plateau
Overfitting / Divergence: The pure NN is memorizing 10-step noise patterns instead of learning physics, and eventually will overfit
Tino
Validation loss should bottom out and then sharply diverge (spike upward) as it loses the ability to generalize across the full trajectory

## Slide 14: Preliminary Results: PyTorch
Tino
The Illusion of Low Loss: These curves demonstrate how the pure neural network (MlpODE) circumvents the noise-dominated data bottleneck. On the left (pytorch, full-shot), the MlpODE rapidly achieves a low loss by treating Voltage as a free variable to memorize the noise, while the physics-anchored models hit a plateau. However, the Loss Curve on the right (10-step window) reveals the inevitable consequence: the MlpODE violently overfits and diverges, confirming its initial success was a mathematical illusion rather than genuine physical learning

## Slide 15: The Roadblock: The Data Bottleneck
Root Cause: The underlying finite-difference Voltage signal is completely noise-dominated (e.g., R2MlpODE ≅ 0.0002)
PyTorch Validation loss curves: Appears to be portraying the same messaging, though further investigation will be needed to confirm
SINDy Dilemma: Applying SINDy to these data residuals will inherit the exact same noise problem
Pivot: We are framing this as a definitive, clean negative result rather than forcing equation discovery on unviable data
Tino

## Slide 16: Primary Goal Assessment
The Goal Was Met: Successfully replicated and even exceeded the baseline reference targets across all three independent approaches
The Not Ideal Reality: Models tracked (Ip , Li ) well, however, are physically questionable and unreliable
Tino

## Slide 17: Next Steps & Feedback
Finalize cross-framework documentation as a strong engineering reproduction of the baseline
Novel dV/dt diagnostic that exposed the limits of the hybrid architecture
Feedback Items
How have peers handled downstream tasks (like equation discovery) becoming mathematically unviable due to dataset noise late in a project?
Tino

## Slide 18: Credit Statement
Tino
Presentation Section | Owner
Intro & Motivation | Christopher Billingham
The Physics Problem: Modeling Plasma Dynamics | Christopher Billingham
AI Methodology: Hybrid Neural ODEs | Phillip Prior
Project Goals & Workflow | Phillip Prior
Preliminary Results: JAX Implementation & SINDy | Phillip Prior
Preliminary Results: Julia Implementation & The Diagnostics | Christopher Billingham
Preliminary Results: PyTorch Implementation & The Second Obstacle | Tino Wells
The Roadblock: The Data Bottleneck | Tino Wells
Project Goal Summary, Next Steps, & Feedback | Tino Wells
Resources | Tino Wells

## Slide 19: Thank You & Resources
Tino
[0] Code base: https://github.com/caderache2014/ENGR521A/
[1] H. Abu-Shawareb et al. (Indirect Drive ICF Collaboration), Achievement of target gain larger than unity in an inertial fusion experiment,"
Phys. Rev. Lett., vol. 132, no. 6, art. no. 065102, Feb. 2024, doi.org/10.1103/PhysRevLett.132.065102
[2] Fusion Industry Association, "The Global Fusion Industry in 2024," Fusion Industry Association, Washington, DC, USA,
Jul. 2024. https://www.fusionindustryassociation.org/fusion-industry-reports/
[3] Anonymous, “Deuterium-Tritium fusion reaction” diagram.
Released into the public domain. Wikipedia Commons: https://commons.wikimedia.org/wiki/File:D-t-fusion.png
[4] M. Greenwald, et al. 20 years of research on the Alcator C-Mod tokamak.
Physics of Plasmas, 21(11):110501, 2014 doi: 10.1063/1.4901920
[5] A. M. Wang, D. T. Garnier, and C. Rea. Hybridizing physics and neural ODEs for predicting plasma inductance dynamics in tokamak fusion reactors.
NeurIPS 2023 Workshop on Tackling Climate Change with Machine Learning. arXiv:2310.20079v1
[6] J. Romero, JET-EFDA Contributors, et al. Plasma internal inductance dynamics in a tokamak.
Nuclear Fusion, 50(100):115002, 2010 doi: 10.1088/0029-5515/50/11/115002